## Slide 1: Ceramics and Glass
https://www.youtube.com/watch?v=tPd1GIwjRFM

## Slide 2: Ceramic/Glass
Describe a Ceramic?
Describe a Glass?

## Slide 3: Ceramic
Inorganic, nonmetallic solid
Metal, nonmetal or metalloid atoms primarily held in ionic and covalent bonds
Brittle, high melting point, poor conductor, stiff, chemically resistant, waterproof
Crystallinity varies from crystalline to semicrystalline to amorphous

## Slide 4: Glass
Inorganic, nonmetallic solid
Metal, nonmetal or metalloid atoms primarily held in ionic and covalent bonds
Brittle, high melting point, poor conductor, chemically resistant, waterproof
Crystallinity: Does not exist i.e. its amorphous also considered a frozen liquid

## Slide 5: Structure
Crystalline Amorphous
http://www.cmog.org/article/what-is-glass

## Slide 6: Ceramics
Ceramic comes from Keramos (Greek for pottery)
Early forms of ceramics were formed by the heat treatment of Clay
E.g. Kaolinite clay after firing above 1000°C forms Porcelain a ceramic
Other forms include
  Earthenware
  Stoneware
  Bone China
A Ming Dynasty porcelain vase dated to 1403–1424
https://upload.wikimedia.org/wikipedia/commons/thumb/4/4f/Blue_and_white_vase_Jingdezhen_Ming_Yongle_1403_1424.jpg/330px-Blue_and_white_vase_Jingdezhen_Ming_Yongle_1403_1424.jpg

## Slide 7: Clay structure
Properties:
With water layers can slide past each other
 plasticity
Upon drying the clay it will harden but no chemical reaction is induced  sundried bricks
Upon firing (>1000°C) can induce chemical bonding of the layers
(formation of Si-O-Si bonds)  Ceramics
Aluminum or Magnesium)

## Slide 8: Ceramics
Another type of ceramic is called a Technical Ceramic
  Oxides
    Quartz (SiO2), Alumina (Al2O3), Ceria (CeO2), Zirconia (ZrO2)
  Nonoxides
    Carbide (e.g. SiC), Nitride (e.g. Si2N4), Silicide (e.g. TiSi2), Boride (Nd2Fe14B)
  Functional Ceramics
    Electroactive, multiferroic, piezoelectric ceramics
    Materials that can convert energy from one form to another or respond in unusual ways to external stimulai (subject of the video)

## Slide 9: Glass
Lets focus on one subset of ceramics ie traditional Glass (leave metallic Glass for later)
Glass is an Amorphous solid
Forms:
Oxides, Borides, Polymers even Metals
Most common glasses are based on SiO2
Moldavite, a natural glass formed by meteor impact, from Besednice, Bohemia
Oldest mouth-blown window-glass in Sweden (Kosta Glasbruk, 1742)
https://anjouclothing.files.wordpress.com/2013/01/7.jpg?w=640
https://s-media-cache-ak0.pinimg.com/236x/cb/e8/6f/cbe86f708b15d1a2c549503c2ba6f5ee.jpg
This course contains copyright materials that are used solely for instructional purposes within this course. Copying, printing or distribution for other purposes is prohibited.

## Slide 10: SiO2
Glass is amorphous ie structure is random in long range
It is inherently unstable so it will crystallize with time (called vitrification)
Melts at 1713°C very high
Given a fire gets no more than 1000°C how did we ever get to develop it?
Si
Si
Si
O
O
O
O
Si
Si

## Slide 11: Earliest Forms
Obsidian
  Volcanic Glass
  Didn’t need a fire
  Used extensively for spearpoints
https://upload.wikimedia.org/wikipedia/commons/thumb/1/17/Lipari-Obsidienne_(5).jpg/225px-Lipari-Obsidienne_(5).jpg

## Slide 12: What about lightning made Glass?
Fulgurites look like this
This is Hollywood’s version
  Sweet Home Alabama
http://slckismet.blogspot.com/2013/03/who-could-have-predicted-that-sweet.html

## Slide 13: History Egypt
King Tutankhamun’s Glass Scarab
Desert Glass was 26M years old so most likely came from a meteorite
Ancient Egyptian faience & glass palace inlays showing Nubian & Philistine slaves (1182-1151 BCE) from Thebes at Museum of Fine Arts. Boston, MA.
http://travelphotobase.com/v/USMAB/MAAF2141.HTM
http://www.gemselect.com/other-info/king-tuts-tomb-of-treasures.php

## Slide 14: What made glass making possible?
The Faience was made by using Nile sediment
This contained Natron (NaCO3)
Sodium is a network modifier
Melts at 850°C and reacts with SiO2
Lower the melting point of glass significantly
Sodium Silicate glass dissolves in water
Add Lime (CaO) to strengthen the network
Thus the invention of Soda lime glass (still used today)

## Slide 15: Brief History
Around 3000BC faience glazes were used
  As fires got hotter one gets more complete reaction
Around 1600BC glass workers started making core wound vessels
By 1500BC glass was in western Asia, Crete, Egypt and Greece
900-600BC new methods in Greece
  Slump Glass and Thousand Flower method
By 100BC glass blowing is developed in Syria /Palestine area
  Made glass inexpensive
  Roman Conquest took technology back to Rome

## Slide 16: Roman Glass
Romans loved Glass
  Made clear colorless glass in Alexandria ~100AD through addition of MnO2
  Drinking vessels
    One of the first times you could see what you were drinking
    Contributed to appreciation of wine
  Made first windows
  Made first mirrors

## Slide 17: History Phoenicia and Rome
400-200BC Phoenician Core wound Vessel
http://sadigh.weebly.com/featured-artifacts/category/amphoriskos
1-100AD Milefiori Roman thousand flower bowl
http://ancientpeoples.tumblr.com/post/61430046465/millefiori-bowl-1-100-ad-roman-glass-source
Roman Mirror
http://mjgrafx.8m.com/Welcome%20to%20Ruby's%20World/RUBYSVILLE/Stories/The%20History%20of%20Mirrors.htm

## Slide 18: European history
Oldest Stain glass 670AD England
Impact on churches was significant
http://northeasthistorytour.blogspot.com/2011/03/oldest-stained-glass-window-in-world.html
Early Murano (Italy) Glass 1330
Ultra pure silica pebbles
http://en.wikipedia.org/wiki/Venetian_glass

## Slide 19: History Continued
1500’s and 1600’s development of telescopes and microscopes
  Revolutionized science and medicine
    Galileo and the solar system
    Leeuwenhook and bacteria
  Offshoot of the printing press?
1608 Jamestown first “industry”
  the first export was glass to England
1959 UK Invention of Float Glass
  Use molten Tin
1970’s development of Fiber optic glass
  Create chlorides and distill
  Repeaters every 18.5 miles, handle 24000 calls/fiber

## Slide 20: Changing the properties of Glass
Glass is brittle
But class is very strong in compression
How does one combine these observations to make glass stronger?
  Rupert Drop
  Corning ware
  Gorilla Glass

## Slide 21: Rupert Drop
http://www.youtube.com/watch?v=xe-f4gokRBs
Origin as early as 1625
Prince Rupert gave them to King Charles II in 1660 who gave them to the Royal Society for study
http://ceramics.org/wp-content/video/rupert_drop.jpg

## Slide 22: Changing the color of glass
Blue - Typically Cobalt <0.1%
Red – metallic Gold 0.001%
- metallic Copper
Yellow – Silver Nitrate,
- Even Uranium
Purple – Manganese
- Nickel
White – Tin oxide with antimony or arsenic oxides
13th-century window from Chartres showing extensive use of the ubiquitous cobalt blue
www.Wikipedia.com
http://www.paradoxplace.com/Photo%20Pages/France/Chartres/Joseph_Window/Images/900/Joseph-upper-middle-Sept07-DE7142sAR900.jpg

## Slide 23: Some typical additives to glass
Na2CO3 (Natron or Soda Ash) network modifier
CaO (lime) network Former
MnO2 masks the green color from iron
Antimony (turn Fe++ to Fe+++) make colorless
PbO (leaded glass) High dispersion crystal
B2O3 (pyrex) low thermal expansion
Al2O3 (aluminosilicate glass) fiberglass
ThO2 Thorium Oxide low dispersion lenses
  (radioactive) no longer used
La2O3 rare earth glass for cameras and telescopes
  (not radioactive)

## Slide 24: Closing thought
As Mark Miodownik observed in his book “Stuff Matters”
  “Perhaps it is because we look through it rather than at it that glass has not become a part of the treasured fabric of out lives. The very thing that we value it for has disqualified it from our affections It is inert and invisible not just optically but culturally”
  However I would add that with the growth of new applications as you will observe with functional ceramics, these materials may indeed become treasured materials for what they can do rather than how they look.

## Slide 25: Additional Modern applications
Float Glass https://www.youtube.com/watch?v=ig4G5WbOMLc
Gorilla Glass https://www.youtube.com/watch?v=wT8xI4PEU8c
Fiber Optics https://www.youtube.com/watch?v=0MwMkBET_5I